## Slide 1
FALL 2026 · READER DECK
Trajectory Extraction, Cross-Embodiment Retargeting & TeleGuide
A research reference pack covering prior work, Panda/UR5e replay, pose uncertainty, budgeted correction, and reproducible experiments.
Reference material for senior CS students
06 October 2026 · v2.0
1 / 31
Notes: This pack is intended for senior CS students and research supporters. Students and supervisors determine the capstone topic, scope, and assessment. IL (Invested Lamda) is the supporter’s current research/prototype priority; this project label is distinct from imitation learning. The update retains the design of the 25 September 2026 reader deck and incorporates evidence available by 6 October 2026. Simulation results do not establish novelty, human benefit, or performance on physical robots.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/README.md

## Slide 2
Purpose and use of this reference pack
CS CAPSTONE REFERENCE
READING OBJECTIVES
01
Assess existing evidence
Run clean-state physics on a CPU. Examine the schema, model receipt, and failure logs before introducing vision.
02
Define a research question
Panda/UR5e transfer and object-relative representations have precedents. The candidate question concerns correction-time allocation.
03
Design a controlled study
Establish that noisy pose inputs affect the plan and task outcome. Distinguish assumed oracle costs from measured human time.
Reference material for students and supervisors, who determine project scope and assessment.
2 / 31
Reader guide and sources
Notes: Read the pack in two passes: first examine scope, pipeline contracts, and results; then consult code, notes, and primary papers for experimental decisions. Reproducing every paper or training a policy is unnecessary for the initial feasibility study. Physics replay begins with clean simulator state. The marker prototype estimates pose from calibrated synthetic pixels. Their integration is incomplete. Implementation, contract tests, pilot observations, and research evaluations represent different levels of evidence.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/README.md

## Slide 3
Shared technical core and distinct objectives
CS CAPSTONE REFERENCE
CURRENT RESEARCH PRIORITY
IL (Invested Lamda)
Reusable pipelines and benchmarks with provenance.
Measured capabilities and execution failures.
Research prototypes before product expansion.
RELATED RESEARCH AND EDUCATIONAL OUTPUTS
CS support and future research
CS: reference code, reading guides, and evidence.
Future study: research questions and controls.
Students and supervisors define capstone scope.
Share code, schemas, and evidence while preserving decision ownership and the scope of each conclusion.
3 / 31
Reader guide and sources
Notes: The shared core comprises video-derived object poses, Panda/UR5e retargeting, segment correction, and budget evaluation. IL receives reusable pipelines, measured capabilities, and engineering decisions. CS students receive reference materials for feasibility assessment. Future research receives testable questions, controls, and an evidence trail. Preserve the label Invested Lamda. This core does not define business requirements, authorize deployment, or impose student assignments.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/evidence-and-limitations.md

## Slide 4
Pipeline contracts and levels of evidence
CS CAPSTONE REFERENCE
Each stage requires its own inputs and metrics. Object pose alone is insufficient to reconstruct a human manipulation task.
Video / robot log
RGB or RGB-D, calibration, timestamps
→
Pose and events
Object/TCP poses, grasp, phases, scale
→
Retargeting
Target IK, controller, contact, constraints
→
Correction
Segment selection, editing, replay, budget
Perception
Pose error, coverage, quality ranking
Kinematics / physics
IK residuals, failure codes, contact
Research endpoint
Task success and human supervision time
4 / 31
Reader guide and sources
Notes: Pose accuracy, kinematic tracking, physics task success, and human benefit are distinct endpoints. Human video additionally requires grasp/contact, TCP orientation, phase, goal, and scale estimation. Robot logs with TCP/gripper state offer a more controlled starting point. The physics reference currently uses a clean TCP trajectory and known target layout. The marker prototype transfers translational displacement through kinematics. Estimated data and evaluator ground truth must remain on separate data paths.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/experimental-protocol.md

## Slide 5
SECTION 01
Simulation reference
Clean-state replay separates frame, grasp, and controller failures from video-estimation errors.
5 / 31
Reader guide and sources
Notes: The current baseline uses MuJoCo on a CPU. Select a simulator according to the research question, available inputs, and reproducibility requirements. Changing the physics engine or controller across methods introduces potential confounding. Isaac may be considered when rendering or parallel learning requirements exceed the current baseline. Such adoption is a proposed extension, not an outcome of a simulator-comparison experiment.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/README.md

## Slide 6
Input assumptions and evaluation objectives
CS CAPSTONE REFERENCE
Human video or robot logs with TCP/gripper state?
Available RGB-D, calibration, and metric CAD?
Rigid-object tasks or richer contact interactions?
Source of target object and goal poses?
Replay, learned-policy, or assisted-success endpoint?
Editing time or total supervision budget?
Independent evaluation episodes and layouts?
These questions guide the choice of prior work and experiments without prescribing a student project.
6 / 31
Reader guide and sources
Notes: Metric scale and coordinate frames require an identifiable reference. A marker requires known size, camera intrinsics/extrinsics, and a marker-to-object transform. A CAD-based method requires consistent geometry and object-frame conventions. Human video does not directly provide robot actions. Describe source and target observations separately: using a ground-truth target pose can isolate source estimation, but it does not evaluate complete perception. Prespecify the primary endpoint and retain unsuccessful trials rather than substituting tracking accuracy for task success.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/README.md

## Slide 7
Implemented MuJoCo reference
CS CAPSTONE REFERENCE
Implemented and tested
Panda source and UR5e + Robotiq 2F-85 target.
6D IK, position servos, and gravity compensation.
Contact physics, a free-joint cube, and trial logs.
Scope of current evidence
One cube and one source demonstration.
Clean simulator state without video estimation.
20 tests passed, with no skipped tests.
CPU reference
Clean pick-and-place
50 development and 100 held-out target layouts. Pinned Menagerie models with a hash receipt.
7 / 31
Reader guide and sources
Notes: Execution uses MuJoCo mj_step, a free-joint cube, and contacts rather than teleporting or welding the object during motion. Resetting the initial state is a separate operation. Menagerie models are pinned at f054586a8e90465d49ee5be15335c4a0c7f57caf. TCP conventions are defined in scene.py. CLI commands verify the model receipt offline; a direct runner.run call does not perform that verification. The review reran 20 tests without skips. This establishes bounded simulation feasibility, not physical-robot safety.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/README.md

## Slide 8
Isaac and larger vision models
CS CAPSTONE REFERENCE
Potential benefits to establish
Rendering or sensing beyond the CPU baseline.
Parallel environments or dexterous tasks.
Mimic/learning for a defined policy endpoint.
Reproducible controllers and input contracts.
Resource requirements and fallback
Pin compatible software, models, and drivers.
Measure memory and runtime on a small input.
Retain CPU replay for failure diagnosis.
Neither reference currently requires GPU rental. New vision or cloud workflows require a separate feasibility pilot.
8 / 31
Reader guide and sources
Notes: These are adoption criteria, not measured superiority of a simulator or an updated minimum-GPU specification. Consult documentation for the exact chosen version and record rendering, controller, asset, and hardware provenance. A learned vision extractor may require a GPU. The marker/PnP and physics references do not. No cloud budget or current rental price is specified here. Retain a CPU replay path to diagnose failures independently of a costly vision stack.
Sources: https://developer.nvidia.com/isaac/lab
Current reference: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/requirements.txt

## Slide 9
Evidence-based expansion of the reference
CS CAPSTONE REFERENCE
9 / 31
Stage | Experimental basis | Required evidence | Current status
P0 · Clean | MuJoCo on CPU | Grasp, transport, release, and logs | Measured: cube / 1 demo
P1 · Noisy | State noise + calibrated video | Noisy inputs affect plan and success | Integration proposed
P2 · Learning | ACT / Diffusion / Isaac as needed | Defined endpoint and usable data | Optional future stage
P0 is available. P1 requires physics integration. P2 depends on a learning or scale endpoint.
Reader guide and sources
Notes: P0 clean replay has been measured for one task and source demonstration. P1 combines noisy-input sensitivity and calibrated video. Phase-local correction requires a representation that actually consumes the relevant intervals. P2 learning or scale is optional and should serve a defined endpoint. The stages are technical recommendations, not official student gates or approval decisions. Do not present an arbitrarily selected threshold as an institutional requirement.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/experimental-protocol.md

## Slide 10
SECTION 02
Literature and research gap
Individual components have precedents. A contribution requires a specific protocol and empirical evidence.
10 / 31
Reader guide and sources
Notes: The literature findings arise from a bounded primary-source audit through 6 October 2026, not an exhaustive systematic review. Citation indexes may lag recent publications. The proposed combined question remains conditional on reviewed-source coverage. Combining existing modules, selecting Panda/UR5e, or using object-relative transforms does not alone establish a research contribution.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/reading-guide.md

## Slide 11
Replay and imitation learning
CS CAPSTONE REFERENCE
Demonstration
Observations, actions, timestamps, labels
→
Behavior cloning
Learn actions from recorded observations
→
Policy rollout
The policy encounters a shifted state distribution
→
Correction data
Interventions with context and outcomes
ACT
Action chunks are an option when the task requires a policy learned from demonstrations.
Diffusion Policy
A model of action distributions. Training requires a suitable schema and a defined endpoint.
MimicGen
A precedent for object-relative demonstration generation. Examine sensitivity to pose noise.
11 / 31
Reader guide and sources
Notes: Retargeting and replay do not train a policy or establish imitation-learning performance. A training export must define observations, action semantics, requested versus executed actions, and sampling rate. A training export would be separate from the physics JSON schema. ACT and Diffusion Policy become relevant when the chosen endpoint includes policy learning. MimicGen is a close precedent for object-relative robot-demonstration transfer. Its noise at subtask initialization differs from drift or missing intervals during motion.
Sources: https://arxiv.org/abs/2304.13705
https://diffusion-policy.cs.columbia.edu/
https://arxiv.org/abs/2310.17596

## Slide 12
Evidence cards for primary papers
CS CAPSTONE REFERENCE
1
Input
RGB, depth, or robot state? What establishes scale and calibration?
2
Output
Object pose, TCP trajectory, joint action, or learned policy?
3
Representation
How does the representation preserve contact or task intent?
4
Human cost
Who reviews, selects, and edits? Is the budget actions, samples, or seconds?
5
Evaluation
Trial units, counts, seeds, holdouts, success criteria, and failures?
6
Limitations
What is explicit, inferred, or still unverified?
12 / 31
Reader guide and sources
Notes: An evidence card should record the exact paper version, section/table/page, code revision, license status, and affected design decision. Separate author statements from interpretations. Rounded success percentages do not identify the sample size without a protocol or raw counts. AUROC/AUPRC measure discrimination; risk–coverage evaluates selective ranking. Probability calibration requires additional analysis. Consult the corrected synthesis and audits before citing values from earlier reports.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/reading-guide.md

## Slide 13
Object-relative transfer and morphology
CS CAPSTONE REFERENCE
Panda and UR5e differ
Arm degrees of freedom: Panda 7, UR5e 6.
Different link lengths, limits, and grippers.
Joint copying does not preserve contact.
Precedents and target constraints
MimicGen includes Panda/UR5e transfer.
The target solves IK using its TCP convention.
Track reachability, joint limits, and singularity.
Evaluate contact success in physics or trials.
Current retargeting uses initial-object and goal anchors. Editing later object poses need not change the plan.
13 / 31
Reader guide and sources
Notes: A common transform is T_target_object × inverse(T_source_object) × T_source_TCP. Panda/UR5e transfer is an experimental setting with precedents. The current physics retargeter segments motion using gripper commands and TCP height, anchors the earlier phase to the first observed object pose before grasp, and anchors the later phase to the goal. Reachability, temporal constraints, collision, and task success require separate reporting. The reference is not a general collision planner, and the cube task does not evaluate orientation-sensitive placement.
Sources: https://arxiv.org/abs/2310.17596
https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/retarget.py

## Slide 14
Automatic recovery: PSI and RIGVid
CS CAPSTONE REFERENCE
CLOSEST AUTOMATIC COMPARATORS
Filtering and backtracking
PSI validates trajectories and grasps in simulation. RIGVid tracks pose and backtracks after deviations. Reproduction requires their methods and input assumptions.
Filtering
Recovery
Pose inputs
BASELINE INTERPRETATION
PSI differs on all/any failed-grasp rejection.
Its 2 cm/0.2 rad threshold belongs to ICP.
RIGVid uses a depth anchor and feedback.
An internal filter requires a separate label.
Automatic recovery and human pose correction differ in information, feedback, and cost. Preserve these distinctions.
14 / 31
Reader guide and sources
Notes: PSI §3.3 describes rejection when all candidate grasps fail, whereas §4.3 describes any grasp failing. The reviewed sources do not resolve this discrepancy in code; a reproduction must disclose its chosen interpretation. Appendix C’s 2 cm/0.2 rad threshold concerns ICP, not a calibrated FoundationPose tracking score. RIGVid uses a generated video and an initial RGB-D frame for depth alignment, with runtime backtracking at 3 cm or 20° deviation. These task-specific values are not universal thresholds. An internally implemented filter should retain its own baseline name.
Sources: https://arxiv.org/pdf/2602.13197v2
https://arxiv.org/abs/2507.00990

## Slide 15
Reliability and budgeted human intervention
CS CAPSTONE REFERENCE
STRUCTURAL PRECEDENTS
ThriftyDAgger and VR-DAgger
Robot-triggered intervention is established. VR-DAgger selects a timestep using action uncertainty, then teleoperates the remainder. Its budget counts correction samples.
LIMITS OF TRANSFER
Meta Pose: rotation failures in individual images.
SPARC: bounding-box annotation reliability.
Neither establishes the utility of object-pose segment selection for retargeted success.
Candidate gap: reliability-guided pose correction with a seconds budget, random selection, and automatic comparators.
15 / 31
Reader guide and sources
Notes: ThriftyDAgger provides a precedent for supervision budgets and autonomous versus assisted endpoints. VR-DAgger proposes three timesteps from MC-dropout action variance; the operator selects one and controls the remainder of the episode. Its correction-sample budget differs from a seconds budget. Meta Pose evaluates image-level rotation failures. SPARC evaluates annotation reliability using bounding-box IoU and downstream VLA reasoning. These targets differ from object-pose segment correction. Failure to find the full combined protocol in inspected sources does not guarantee field-wide novelty.
Sources: https://proceedings.mlr.press/v164/hoque22a.html
https://arxiv.org/abs/2605.27114
https://arxiv.org/abs/2608.03516
https://arxiv.org/abs/2606.13497

## Slide 16
Reading sequence and design decisions
CS CAPSTONE REFERENCE
16 / 31
Design question | Priority reading | Evidence to inspect
Representation | MimicGen | Object anchors, Panda/UR5e, pose-noise Appendix U
Automatic recovery | PSI · RIGVid | Rejection/grasp rules, depth anchors, backtracking
Human budget | ThriftyDAgger · VR-DAgger | Actions/samples/seconds, review cost, controls
Reliability | Meta Pose · SPARC · ProxyPose | Failure labels, scale, and task sensitivity
Learning (optional) | ACT · Diffusion Policy | Observations/actions, loaders, policy endpoint
Inspect experiments, appendices, and code. Separate explicit claims, interpretations, and unresolved evidence.
Reader guide and sources
Notes: Prioritize experiments, appendices, and executable code over abstracts. For robot logs, begin with MimicGen. For video-derived object trajectories, examine PSI/RIGVid and DemoBridge. For correction allocation, read ThriftyDAgger, VR-DAgger, and FlowCorrect. Examine the actual reliability targets of Meta Pose and SPARC. UMI and Human2Sim2Robot are additional readings when their inputs and embodiments match the project. Human2Sim2Robot is arXiv 2504.12609 and uses an Allegro hand; the UMI paper names UR5. Learning architectures remain optional after a suitable data contract exists.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/reading-guide.md

## Slide 17
SECTION 03
Experiments and reference results
Noisy inputs must affect the plan and task outcome before correction-allocation strategies can be evaluated.
17 / 31
Reader guide and sources
Notes: The clean-state benchmark establishes feasibility of a particular replay/controller pipeline on a cube task. It does not test reliability-guided correction. Oracle pilots can validate data plumbing and input sensitivity. A subsequent human study is required to measure correction-time allocation or operator benefit. Distinguish those proposed experiments from existing results throughout the presentation.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/README.md

## Slide 18
Candidate research question
CS CAPSTONE REFERENCE
For a correction budget of B seconds, does reliability-guided segment selection improve task success over random selection and automatic recovery?
Correction target
Video-derived object poses. Separate global biases from local failures.
Controlled comparison
Shared candidates, edit primitives, controller, and budget accounting.
Primary endpoint
Task success after retargeting. Include a GT-assisted oracle comparison.
The question remains untested. A negative result is informative after protocol and input sensitivity are established.
18 / 31
Reader guide and sources
Notes: The proposed primary estimand is the task-success difference between ranked and random correction under a common cost definition. Automatic recovery uses no human editing but incurs runtime costs; report its cost and coverage separately. A ground-truth-assisted oracle is an empirical comparator, not a guaranteed success upper bound. Pose-error ranking need not optimize task success. Prespecify whether B covers active editing or total review plus editing. Select budgets and sample size from pilot variability and required precision. Fit scores/thresholds on development data and evaluate on independent episodes, corruptions, and layouts.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/reading-guide.md

## Slide 19
Pose inputs and data contracts
CS CAPSTONE REFERENCE
1 · Input
Calibration, timestamps, scale provenance
→
2 · Estimate
SE(3), validity mask, diagnostics
→
3 · Events
TCP, gripper, phases, and goal
→
4 · Retarget
Requested plan and executed states
→
5 · Evaluate
Task criteria, failures, and cost
Frame conventions
T_A_B maps B to A. Use metres, seconds, and wxyz quaternions. Retain missing frames.
Ground-truth isolation
GT enters the evaluator/oracle only. Estimated poses must reach the planner without a clean-state shortcut.
Training export
LeRobot/HDF5 requires an adapter and loader roundtrip. Physics JSON alone is not an ACT/Diffusion dataset.
19 / 31
Reader guide and sources
Notes: physics_replay.episode.v1 requires increasing timestamps, TCP/object position_m and wxyz quaternions, gripper commands, scene conventions, and robot joints. Missing object poses are complete null/NaN rows; the robot’s own TCP log cannot omit frames. The marker package stores observations, evaluator GT, and correction receipts separately. Their adapter is not implemented. Training export requires observation/action definitions, requested versus executed actions, synchronization, authority labels, and correction provenance. Avoid exposing evaluator GT as an observation. An estimator with unresolved scale needs an independent metric reference.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/episode.py
https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/marker-prototype.md
https://arxiv.org/html/2607.06555v1

## Slide 20
Clean-state physics: held-out results
CS CAPSTONE REFERENCE
20 / 31
Method | Success / N | Wilson 95% CI | Failures
World-frame | 0 / 100 | 0.00–3.70% | 94 grasp, 2 drop, 4 place
Object-relative | 89 / 100 | 81.37–93.75% | 11 IK failures
Object-relative trimmed | 100 / 100 | 96.30–100.00% | None in this sample
Target scripted reference | 100 / 100 | 96.30–100.00% | None in this sample
One cube, one source demonstration, 100 target layouts at seed 7. Clean state without video or correction.
Reader guide and sources
Notes: The committed held-out log contains 100 paired target layouts at seed 7, four methods, one source demonstration, and one cube task. Development results on 50 layouts were 0/41/50/50; the trimmed variant was refined using that set. Object-relative held-out execution has 11 IK failures. World-frame has 94 grasp failures, two drops, and four placement misses. The scripted target reference has task-specific knowledge. Wilson 95% intervals use z=1.96 under the binary-trial assumption within the sampled domain. The predicate includes lift ≥5 cm, final XY error ≤2 cm, z error ≤5 mm, uprightness, and release with failure flags. It lacks a velocity/dwell criterion and goal-yaw requirement. The review recomputed logs and verified code hashes without rerunning all 600 trials.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/tree/main/physics_replay/results/bench-heldout-seed7-n100
https://www.itl.nist.gov/div898/handbook/prc/section2/prc241.htm

## Slide 21
Module contracts and integration
CS CAPSTONE REFERENCE
21 / 31
Module | Principal contract | Implementation status
Physics replay | TCP/object/goal, grasp command, task criteria | Clean demonstration and benchmark
Video / marker | Pixels, calibration, estimates, validity mask | Synthetic/PnP pilot; translation only
Retarget input | Initial object anchor + TCP/goal trajectory | 65 edited pose frames leave plan unchanged
Correction / cost | Edited artifacts, candidates, time receipts | Assumed oracle cost; terminal editor
Bridge / export | Consequential pose inputs, physics, labels | End-to-end integration remains absent
The missing bridge: edited inputs must alter the plan before downstream success can be assessed.
Reader guide and sources
Notes: The table defines technical boundaries and status, not student ownership assignments. Physics and marker packages are separate. A bridge must reconcile TCP/object frames, events, and observable inputs. In the example episode, adding 0.05 m to x in 65 observed object frames after the first observed frame leaves the object_relative_trimmed TCP plan exactly unchanged. This was a plan-sensitivity probe, not a physics run or benefit measurement. The static-anchor path does not consume those later poses. Phase-local constraints are a potential representation extension requiring independent validation.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/retarget.py
https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/evidence-and-limitations.md

## Slide 22
SECTION 04
TeleGuide and correction budgets
An intervention must produce a replayable correction artifact, time records, and an observable outcome.
22 / 31
Reader guide and sources
Notes: TeleGuide here denotes research support for trajectory review and correction. The starter contains standalone physics and marker references. A web interface and a validated pose/physics user study are outside its current scope. An interface or pause/takeover demonstration cannot establish usability or labour savings. Simulation alone cannot establish safety of physical intervention.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/marker-prototype.md

## Slide 23
Review, correction, and reusable data
CS CAPSTONE REFERENCE
REVIEW
Inspect context and intent
Pose axes, diagnostics, source frames, and candidate segments. Record review and selection time.
CORRECT
Use a shared edit primitive
Offsets, waypoints, or phases under a defined contract. Save a new artifact and preserve the original.
REPLAY
Outcome and provenance
Retarget again and retain failures. Record authority labels when exporting training data.
The terminal editor measures session elapsed time. Active editing, review, and waiting remain unseparated.
23 / 31
Reader guide and sources
Notes: The terminal editor saves a new NPZ and a monotonic-clock receipt. The candidate segment is selected through the CLI before the clock starts. The response interval includes reading, waiting, and input, so session elapsed time does not isolate active editing. Overruns are rejected. A constant offset changes valid frames only and does not recover missing poses. A user study requires matched primitives, costs, observable information, and counterbalanced condition order. A future authority-label adapter requires its own contract before research data can train a policy.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/marker-prototype.md
https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/evidence-and-limitations.md

## Slide 24
Manipulation demonstration in MuJoCo
CS CAPSTONE REFERENCE
Engineering evidence
Panda source, UR5e target.
Contact physics.
Clean simulator state.
Predicate-based success.
Not yet evaluated
Video/correction is not integrated with physics. No human study or real-robot evaluation.
24 / 31
Panda source · simulator state
UR5e trimmed · contact physics
Reader guide and sources
Notes: The images are frames from existing simulator recordings, not physical-robot photographs. Both runs execute manipulation through contact physics. Images illustrate behaviour; quantitative conclusions depend on trial logs. The README records a user-run Colab CPU evaluation on 6 October with 20 passing tests and success/failure agreement for 200 development and 400 held-out trials. This review did not independently rerun Colab. Integrated video correction and human benefit remain unevaluated.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/README.md
Image provenance: frames at t=6s from the source and target MuJoCo recordings. The source revision and associated reference results are identified in provenance.json. The videos can be recreated with the physics demo.

## Slide 25
A protocol with matched correction budgets
CS CAPSTONE REFERENCE
Candidate pool
Segments, lengths, costs, validity
→
Conditions
Automatic, random, ranked, oracle
→
Correction
Shared primitive and observable information
→
Retarget/replay
Shared layouts, controller, success criteria
Reported measurements
Task success, rejects, review/edit/wait/total time, pose error, and failure taxonomy.
Human-cost comparison
Active-time reduction requires measured full teleoperation at matched task quality.
25 / 31
Reader guide and sources
Notes: Prespecify B, candidate intervals, lengths, edit primitives, replay/feedback access, start/stop events, and overrun handling. If B counts active editing, also report review, waiting, and total supervision. Active-human-time reduction can be defined as 1 - T_active_assisted/T_active_fullteleoperation, requiring a measured baseline with matched task quality. Define system-latency endpoints explicitly, for example edit submission to plan preview or controller acknowledgement, and report p50/p95. Evaluate pose-quality signals on held-out errors before studying downstream failures. Retain rejects, timeouts, and failures. Account for episode/operator dependence rather than treating frames as independent samples. Future tuning requires a new held-out set because seed 7 outcomes are already known.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/experimental-protocol.md
https://proceedings.mlr.press/v164/hoque22a.html

## Slide 26
Resources, risks, and contingency measures
CS CAPSTONE REFERENCE
26 / 31
Risk | Contingency / diagnostic | Retained evidence | Status
Poor poses / occlusion | Validity mask, filtering, manual edit | Original/estimated/corrected data + reasons | Proposed physics integration
Clean replay failure | Frame/TCP, grasp, controller, IK | Failure logs and reduced task scope | Reference available for diagnosis
Idle GPU / cost | Heartbeat, checkpoint, then stop | Runtime/cost ledger and receipt | Operational measures proposed
Data / checkpoints | Hashed local cache; selective sync | Manifest, version, retention policy | Storage procedure proposed
The CPU reference is available. Cloud idle-timeout and caching procedures remain proposed.
Reader guide and sources
Notes: The reference workflows run on a CPU. Idle-timeout control is proposed, not implemented. Use a workload heartbeat and active-job check, save checkpoints before termination, and log stop events. Low GPU utilization alone may reflect CPU preprocessing. Local dataset/checkpoint caches require manifests, hashes, versions, selective synchronization, and explicit retention. Diagnose clean replay failures through frames/TCP/grasp/controller/IK residuals and reachability before adding perception. Retain missing masks and correction provenance under occlusion. Kalman or particle filtering requires a defensible measurement model. No cloud budget or current GPU price is asserted.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/README.md
https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/README.md

## Slide 27
An experimental sequence
CS CAPSTONE REFERENCE
STEP A
Pose sensitivity
Consequential clean/corrupt inputs.
Anchor, frame, and scale assumptions.
Failure logs and physics replay.
STEP B
Correction protocol
Edited artifacts alter the plan.
Random/ranked use matched budgets.
Oracle pilot, then measured human time.
STEP C
Calibrated video
Markers or RGB-D with a reference.
Occlusion and scale diagnostics.
Markerless estimation when feasible.
Clean replay failure: examine frames, TCP, grasp, controller, and IK before expanding scope.
27 / 31
Reader guide and sources
Notes: The sequence reflects dependencies, not mandatory deadlines or assignments. Sensitivity experiments must perturb planner inputs that are actually consumed. A static anchor is insufficient for allocation over intervals that cannot influence the output. A phase-dependent representation needs its own tests. Following oracle plumbing, a human pilot estimates variability and cost. The current video importer assumes constant frame rate through frame_index/fps and does not handle variable-rate timestamps. Synthetic-fixture calibration is not calibration of a physical camera. Assembly, deformation, or bimanual manipulation are optional later stress tests, not additions required for the first baseline.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/experimental-protocol.md

## Slide 28
Evidence checklist for the reference pack
CS CAPSTONE REFERENCE
Technical resources
Clear CPU setup and run commands.
Schema and model/config/code hashes.
Example episodes and per-trial failures.
Clean replay across two embodiments.
Videos and results with explicit scope.
Research resources
Closest works and verified corrections.
Research questions, controls, and budgets.
Trial definitions and uncertainty.
Negative results and limitations.
Proposed, tested, and evaluated states.
This checklist supports reproducibility. It does not replace the institution’s capstone assessment criteria.
28 / 31
Reader guide and sources
Notes: Passing implementation tests is distinct from empirical method superiority. Physics has 20 tests, committed trial logs, and model receipts. The marker package has seven tests and a synthetic pilot, with no independent inspection verdict. Model caches, generated runs, and canonical literature PDFs are excluded from Git and require recreation or separate retrieval. Do not generalize from 100 layouts of one demonstration. No human study has been conducted. A null result should report failures, coverage, time costs, and sensitivity checks so rival explanations can be assessed.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/evidence-and-limitations.md
https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/evidence-and-limitations.md

## Slide 29
Repository execution paths
CS CAPSTONE REFERENCE
Physics reference
Python 3.12 in a separate environment.
pip install -r physics_replay/requirements.txt
python -m physics_replay fetch-models
python -m physics_replay demo
python -m pytest -q physics_replay/tests
Marker / correction prototype
Separate environment: requirements-research.txt.
python tools/research-prototype.py fetch-models
python tools/research-prototype.py demo
A new output directory for each run.
See docs/marker-prototype.md.
Public starter repository. Separate environments and endpoints. End-to-end integration remains absent.
29 / 31
Reader guide and sources
Notes: Run physics commands from the repository root in an activated environment. Fetch models once, then execute the demo, example replay, benchmark, and pytest. The CPU Colab notebook clones this public starter without requiring a code upload or GitHub authentication. The marker package uses a separate Python 3.12 environment with requirements-research.txt. Run unittest discovery in tests/research_pipeline and demo --output data/research-prototype/runs/my-demo, where the output directory must not exist. Ground truth, observations, and receipts are separate. The default 20-second budget and 10-second oracle edit cost are assumptions, not observed human times. Do not combine the differently pinned environments without resolving dependencies.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/physics_replay/README.md
https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/marker-prototype.md

## Slide 30
Resources: repository and documentation
CS CAPSTONE REFERENCE
Links provide code, notebooks, committed results, and reproducibility guidance.
Executed reference
Public code, notebook, and reference results. Run manifests retain model, configuration, and code hashes.
Reading and provenance
Consult the README, proof status, and reports before citing a numerical result or research claim.
30 / 31
Physics README
physics_replay/README.md
Colab CPU notebook
Open the public CPU notebook
Held-out results
results/bench-heldout-seed7-n100
Example episode
panda_pick_place_10hz.json
Reader guide and sources
docs/reader-guide.md
Marker / correction
docs/marker-prototype.md
Reading guide
docs/reading-guide.md
Reader guide and sources
Notes: The public starter offers a selected snapshot with a fresh Git history. The imported runtime code and benchmark manifests retain their provenance and hashes in provenance.json. The repository contains the reader deck, its PDF, and this companion guide. Model caches, generated runs, and scientific-paper PDFs are excluded from Git. Match runtime hashes when comparing reruns with the reference outcomes.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/provenance.json
https://github.com/loversky02/trajectory-retargeting-starter/blob/main/README.md

## Slide 31
Resources: primary papers
CS CAPSTONE REFERENCE
Read the relevant versions, experiments, appendices, and code. Novelty remains conditional on source coverage.
Representation and recovery
Prioritize MimicGen, PSI, and RIGVid for the chosen inputs. Defaults do not establish paper trial counts.
Reliability and intervention
Sample/action budgets differ from seconds. Pose ranking alone does not establish task utility.
31 / 31
MimicGen
https://arxiv.org/abs/2310.17596
PSI
https://arxiv.org/abs/2602.13197v2
RIGVid
https://arxiv.org/abs/2507.00990v3
ThriftyDAgger
https://arxiv.org/abs/2109.08273
ProxyPose
https://arxiv.org/abs/2607.06555v1
VR-DAgger
https://arxiv.org/abs/2605.27114v2
Meta Pose
https://arxiv.org/abs/2608.03516v1
SPARC
https://arxiv.org/abs/2606.13497v1
ACT / ALOHA
https://arxiv.org/abs/2304.13705
Diffusion Policy
https://diffusion-policy.cs.columbia.edu/
Reader guide and sources
Notes: Primary references include MimicGen 2310.17596, PSI 2602.13197v2, RIGVid 2507.00990v3, ThriftyDAgger 2109.08273, VR-DAgger 2605.27114v2, Meta Pose 2608.03516v1, SPARC 2606.13497v1, and ProxyPose 2607.06555v1. ProxyPose aligns benchmark depth to GT in the first frame; robot replay needs an independent scale reference. Rounded percentages do not identify Mirage’s N. Compatibility with k/186 does not establish one execution per CosmoH2G case. Cases sharing an object may be dependent. Consult the synthesis for ACT, Diffusion Policy, UMI, and Human2Sim2Robot.
Sources: https://github.com/loversky02/trajectory-retargeting-starter/blob/main/docs/reading-guide.md